## Slide 1: Control of Manufacturing Processes
  David Hardt
  October 30, 2013
Manufacturing

## Slide 2: Topics for Today
Physical Origins of Variation
  Process Sensitivities
Statistical Models and Interpretation
  Process as a Random Variable(s)
  Diagnosis of Problems
Shewhart Charts
Process Capability
Next Steps: Optimization and Control

## Slide 3: Process Objectives?
Rate
Quality
Cost
Flexibility

## Slide 4: Process Control Objectives?
Rate
Quality
  Conformance to Specifications wrt
    Geometry
    Properties
Cost
Flexibility

## Slide 5: Lab Processes
CNC Turning
Critical Dimension:
Shaft Diameter

## Slide 6: Lab Processes
Brake Bending
Critical Dimension:
Part Angle

## Slide 7: Lab Processes
Injection Molding
Critical Dimension:
?

## Slide 8: Lab Processes
Thermoforming
Critical Dimension:

## Slide 9: Other Related Problems: Cost, Rate and Flexibility:
100% inspection with high scrap rates
  low throughput
  high costs
100% Inspection with frequent rework
  low throughput
  high costs
High Variability at changeover
  Reluctance to changeover
  low flexibility

## Slide 10: Manufacturing Processes
How are they defined?
How to they do their thing?
How can they be categorized?
Why don’t they always get it right?

## Slide 11: Origins of Variation

## Slide 12: The Process Components
Equipment
Workpiece Material
Operator
Part
Etch bath
Injection Molder
Lathe
Draw Press
...
Coated Silicon
Plastic Pellets
Bar stock
Sheet Metal
...
Semiconductor
Connector Body
Shaft
Hood
...

## Slide 13: What Causes Variation in the Process Output?
Material Variations
  Properties, Initial Geometry
Equipment Variations
  Non-repeatable, long term wear, deflections
Operator Variations
  Inconsistent control, excessive “tweaking”
“Environment” Variations
  Temperature and Handling inconsistencies

## Slide 14: Can We Rank These?
Likelihood of Variation?
Frequency of Variation?
Magnitude of Variation?
Sensitivity to Variation?

## Slide 15: Can We Rank These?
Equipment
  Fixed “Iron”
  Can be Automated (Controlled) to Keep Energy States as Desired
Material
  “Flows” Through the Process
    Constantly Changing
  Energy Transfer from Equipment Variable

## Slide 16: Process Control Hierarchy
Identify and Reduce Disturbances
  Good Housekeeping (Ops Management)
  Standard Operations (SOP’s)
  Statistical Analysis and Identification of Sources
  Feedback Control of Machines
  Reduce Sensitivity (Process Optimization or Robustness)
  Measure Sensitivities via Designed Experiments
  Adjust “free” parameters to minimize
Measure output and manipulate inputs
  Feedback control of Output(s)

## Slide 17: Why not Always “Process Output Control”?
Lack of Measurements
  Shape not accessible
Lack of Spatial Resolution
  Complex shape, simple control u
Cost/Benefit vs. Other Methods
Sufficiency of Equipment Control
  e.g. numerical control

## Slide 18: Modeling Variation

## Slide 19: Applying Statistics to Manufacturing: The Shewhart Approach (circa 1925)*
All Physical Processes Have a Degree of Natural Randomness
A Manufacturing Process is a Random Process if all “Assignable Causes” (identifiable disturbances) are eliminated
A Process is “In Statistical Control” if only “Common Causes” (Purely Random Effects) are present.
W.A. Shewhart, “The Applications of Statistics as an Aid in Maintaining Quality of a Manufactured Product”, Journal of the American Statistical Association, 20, No.. 152, Dec. 1925.

## Slide 20: Shewhart Applied to Manufacturing
Measure and Plot the Process Output
Look for Any Sign of Non-Random (Deterministic) Behavior
  Out of Statistical Control
Identify the Cause of that Behavior and Reduce or Eliminate it
Verify That the Process is NowPurely Random
  In Statistical Control

## Slide 21: Statistical Models for Manufacturing

## Slide 22: Consdier: Turning Process

## Slide 23: Observations from Experiments
random or unknown
Da
Randomness + Deterministic Changes

## Slide 24: Brake Bending of Sheet
Output:
Angle

## Slide 25: Bending Process
Springback

## Slide 26: Observations from Bending Process
Angle changes with depth
DY -> Du
Clear Input-Output Effects (Deterministic)
Also Randomness as well

## Slide 27: Observations from Injection Molding

## Slide 28: Consider: No Effective Changes (¶Y/¶u= 0)
Injection Molding Entire Run

## Slide 29: Injection Molding (S’2003)

## Slide 30: How To Model to Distinguish these Effects?
Inputs
A Random Process + A Deterministic Process

## Slide 31: Random Processes
Consider the Output-only, “Black Box” view of the Run Chart
How do We Characterize The Process?
  Using Y(t) only
WHY do we Characterize the Process
  Using Y(t) only?
Process
Y(t)

## Slide 32: How to Describe Randomness?
Look at a Frequency Histogram of the Data
Estimates likelihood of certain ranges occurring:
      Pr(y1 < Y <y2)
      “Probability that a random variable Y falls between the limits y1 and y2”

## Slide 33: Analysis of Histograms
Is there a consistent pattern?
Is an underlying “parent” distribution suggested?

## Slide 34: Process Outputs as a Random Variable
The Histogram suggests a pdf
  Parent or underlying behavior “sampled” by the process
Standard Forms (There are many)
  e.g. The Uniform and Normal pdf’s

## Slide 35: Histogram for CNC Turning

## Slide 36: Histogram for Bending (MIT 2002 data)
0.3 in depth only

## Slide 37: Histogram for Bending (MIT 2002 data)
0.6 in depth only

## Slide 38: Conclusion?
When there are no input effect (no Du or ¶Y/¶u) a consistent histogram pattern can emerge
How do we use knowledge of this pattern?
  Predict behavior
  Set limits on “normal” behavior
Define analytical probability density functions

## Slide 39: Underlying or “Parent” Probability
A model of the “true”, continuous behavior of the random process
Can be thought of as a continuous random variable obeying a set of rules (the probability function)
We can only glimpse into these rules by sampling the random variable (i.e. the process output)
Underlying process can have
  Continuous Values (e.g. geometry)
  Discrete Values (e.g. defect occurrence)

## Slide 40: The Uniform Distribution
r
x
p(x)
1/r
x1
x2

## Slide 41: Standard Normal Distribution
z

## Slide 42: Continuous Distribution: Normal or Gaussian
cdf
0
0.16
0.5
0.84
1
pdf

## Slide 43: Properties of the Normal pdf
Symmetric about mean
Only two parameters:
  m and s2
Superposition Applies:
  sum of normal random variables has a normal distribution

## Slide 44: Interpretation of the PDF: Confidence Intervals
68%
95%
99.7%
Probability that |x| >m+3s = 3/1000

## Slide 45: Model Calibration
For the Normal PDF, we need two parameters: m and s
We have to estimate m and s using sample statistic based on samples of the output (i.e. measurements)

## Slide 46: Sample Statistics

## Slide 47: Conclusions
All Physical Processes Have a Degree of Natural Randomness
We can Model this Behavior using Probability Distribution Functions
We can Calibrate and Evaluate the Quality of this Model from Measurement Data using appropriate Sample Statistics

## Slide 48: In-Control (Almost)

## Slide 49: Not In-Control

## Slide 50: “Not In-Control”

## Slide 51: “In-Control”
i
i+1
i+2
...
The Parent Distribution Does Not Change with Time
Time

## Slide 52: “Not In-Control”
i
i+1
i+2
...
The Parent Distribution Changes with Time
Time

## Slide 53: “Not In-Control”
...
Time
Mean Shift
Mean Shift + Variance Change
Variance Increase

## Slide 54: Applying in Real-Time: Xbar and S Charts
Shewhart:
  Plot sequential average of process
    Xbar chart
    Distribution?
  Plot sequential sample standard deviation
    S chart

## Slide 55: Data Sampling and Sequential Averages
n measurements
at sample j
sample interval DT
Given a sequence of process outputs xi:
j j+1 j+2 ...
A sequential sample of size n
Take at intervals DT
Sample index j

## Slide 56: Data Sampling
sample j mean
sample j variance
n measurements
at sample j
sample interval DT
j j+1 j+2 ...

## Slide 57: Plot of xbar and S Random Data n=5
xbar
S

## Slide 58: Overall Statistics
Grand Mean
Grand Standard Deviation

## Slide 59: Setting Chart Limits
Expected Ranges
Confidence Intervals
  Intervals of + n Standard Deviations
  Most Typical is + 3s

## Slide 60: Chart Limits - Xbar
If we knew sx then:
But Since we Estimate the Sample Standard Deviation, then
(Sj is a biased estimator)

## Slide 61: Chart Limits xbar chart
The estimate of True Sample Mean Variance (variance of the mean) is biased
To remove this bias for the xbar ± 3s limits we use:
For the example n=5

## Slide 62: Chart Limits S
The variance of the estimate of S can be shown to be:
So we get the chart limits:

## Slide 63: Example xbar
UCL
LCL
Grand
Mean

## Slide 64: Example S
UCL
LCL
Grand S

## Slide 65: Detecting Problems from Running Data
Appearance of data
  Confidence Intervals
  Frequency of extremes
  Trends

## Slide 66: Western Electric Rules
Points outside limits
2-3 consecutive points outside 2 sigma
Four of five consecutive points beyond 1 sigma
Run of 8 consecutive points on one side of center

## Slide 67: Test for “Out of Control”
Extreme Points
  Outside ±3s
Improbable Points
  2 of 3 >±2s
  4 of 5 >± 1s
  All points inside ±1s

## Slide 68: Tests for “Out of Control”
Consistently above or below centerline
  Runs of 8 or more
Linear Trends
  6 or more points in consistent direction
Bi-Modal Data
  8 successive points outside ±1s

## Slide 69: Applying Shewhart Charting
Find a run of 25-50 points that are “in-control”
Compute chart centerlines and limits
Begin Plotting subsequent xbarj and Sj
Apply rules, or look for trends, improbable events or extremes.
If these occur, process is “out of control”

## Slide 70: Real-Time
Historical Data
The “Future”

## Slide 71: Out of Control
Data is not Stationary
  (m or s are not constant)
Process Output is being “caused” by a disturbance (common cause)
This disturbance can be identified and eliminated
  Trends indicate certain types
  Correlation with know events
    shift changes
    material changes

## Slide 72: “In-Control”
i
i+1
i+2
...
What will chart look like?
Time

## Slide 73: “Not In-Control”
i
i+1
i+2
...
Time
What will chart look like?

## Slide 74: Another Use of the Statistical Process Model: The Manufacturing -Design Interface
We now have an empirical model of the process
m
+3s
-3s
How “good” is the process?
Is it capable of producing what we need?

## Slide 75: Process Capability
Assume Process is In-control
Described fully by xbar and s
Compare to Design Specifications
  Tolerances
  Quality Loss

## Slide 76: Design Specifications
Tolerances: Upper and Lower Limits
Characteristic
Dimension
Target
x*
Upper Specification Limit
USL
Lower Specification Limit
LSL

## Slide 77: Design Specifications
Quality Loss: Penalty for Any Deviation from Target
QLF = L*(x-x*)2
x*=target
How to Calibrate?

## Slide 78: Use of Tolerances: Process Capability
m
+3s
-3s
x*
USL
LSL
Define Process using a Normal Distribution
Superimpose x*, LSL and USL
Evaluate Expected Performance

## Slide 79: Process Capability
Definitions
Compares ranges only
No effect of a mean shift:

## Slide 80: Process Capability: Cpk
= Minimum of the normalized deviation from the mean
Compares effect of offsets

## Slide 81: Cp = 1; Cpk = 1

## Slide 82: Cp = 1; Cpk = 0

## Slide 83: Cp = 2; Cpk = 1

## Slide 84: Cp = 2; Cpk = 2

## Slide 85: Effect of Changes
In Design Specs
In Process Mean
In Process Variance
What are good values of Cp and Cpk?

## Slide 86: Cpk Table
Cpk | z | P<LS or
 |  | P>USL
1 | 3 | 1E-03
1.33 | 5 | 3E-07
1.67 | 4 | 3E-05
2 | 6 | 1E-09

## Slide 87: The “6 Sigma” problem
+3s*
-3s*
USL
LSL
6s
P(x > 6s) = 18.8x10-10
Cp=2
Cpk=2

## Slide 88: The 6 s problem: Mean Shifts
USL
LSL
4s
P(x>4s) = 31.6x10-6
Cp=2
Cpk=4/3
Even with a mean shift of 2s
we have only 32 ppm out of spec

## Slide 89: Capability from the Quality Loss Function
QLF = L(x) =k*(x-x*)2
Given L(x) and p(x) what is E{L(x)}?
x*

## Slide 90: Expected Quality Loss
Penalizes Variation
Penalizes Deviation

## Slide 91: Process Capability
The reality (the process statistics)
The requirements (the design specs)
Cp - a measure of variance vs. tolerance
Cpk a measure of variance from target
Expected Loss- An overall measure of goodness

## Slide 92: Process Control Hierarchy
Identify and Reduce Causal Disturbances
  Good Housekeeping
  Standard Operations (SOP’s)
  Feedback Control of Machines
    Eliminate Equipment Variations
  Statistical Analysis and Identification of Sources (SPC)
    Eliminate Assignable Causes

## Slide 93: Process Control Hierarchy
NEXT: Reduce Sensitivity to Disturbance
  Measure Sensitivities via Designed Experiments (DOE)
  Adjust “free” parameters to minimize variations

## Slide 94: Example: Bending Sensitivity to Yield Stress
  Simple Example: Die Width for Air Bending (An adjustable equipment property):
  Wide Die:
    Low force,
    high spring back,
    high sensitivity to variations in yield stress
  Narrow Die:
    High force,
    Higher material stress,
    Lower spring back,
    Lower sensitivity to variations in yield stress,

## Slide 95: Final Step :“Output Control”
Equipment
Material
Geometry &
Properties
“critical dimensions”
C
Desired
Output
Examples:
Web Thickness in Milling
Sheet Thickness in Rolling
Sheet Angle in Bending

## Slide 96: Implementing Product Feedback Control
Continuous In-Process Measurements
  Regulate Process States In-Process
Sampling and Monitoring (SPC)
  Measure After-Process and Diagnose
Part to Part Sampling and Control
  Cycle to Cycle Control: Measure After each Cycle and Improve Process Capability

## Slide 97: Conclusions: Single Variable Case
Cycle to Cycle Control
  Obeys Root Locus Prediction wrt Dynamics
  Amplifies White Noise Disturbance Attenuates Colored Noise Disturbance
  Can Reduce Mean Error (Zero if I-control)
  Can Reduce “Open Loop” Expected Loss
T
Lower Spec
Upper Spec

## Slide 98: Feedback Control Objectives
Steady-State Error from Target
Target
Disturbance Rejection

## Slide 99: It Works!: Bending Step Disturbance
Effect of Material Change
  Switch to a Stiffer Material – more springback.

## Slide 100: Manufacturing Objective
Process
Design Goal
LSL T USL
Process Output
Method?:
  SPC
  Optimization
  Output Feedback

## Slide 101: Conclusions
Shewhart Charts
  Application of Statistics to Production
  Plot Evolution of Sample Statistics and S
  Look for Deviations from Model
Process Capability
  A measure of the process to meet a requirement
  Includes variance and bias
  Gets design and manufacturing talking
If That’s Not Good Enough
  DOE/Optimization
  Feedback Control
  …