ATTACHMENT 4

TECHNICAL DATA PACKAGE (TDP)

CONTRACT REQUIREMENTS

for the

Intermediate Level

Test Program Sets (TPS)/

Operational Test Program Sets (OTPSs)

DISTRIBUTION STATEMENT A.  Approved for public release; distribution is unlimited.

Table of Contents

Section	Title

1.	SCOPE

1.	Scope

2.	APPLICABLE DOCUMENTS

2.1		Documents

3.	REQUIREMENTS

3.1	Technical data package (TDP)

3.1.1		Existing data products

3.1.2		Language

3.1.3		Units of measure

3.1.4		Supplemental requirements

3.1.4.1		Indentured data lists

3.1.4.2		Vendor items

3.1.4.3		Source control drawings (SCDs)

3.1.4.4		Circuit Card Assemblies (CCA) Drawings

4.	PREPARATION AND MANAGEMENT RESPONSIBILITY

4.1		Drawing revisions

4.2		Conferences, reviews, and audits

4.2.1		TDP guidance conference

4.2.2		In-process reviews

4.2.3		Physical configuration audit (PCA)

4.2.4		Final technical review for digital deliveries

4.2.5		TDP discrepancy notification and correction

4.2.6		Data and equipment

List of Enclosures

Enclosure 1 - TDP Option Selection Worksheet - Product Drawings and Associated Lists

1.  SCOPE

1.1  Scope.  This attachment describes the Technical Data Package (TDP) requirements for Operational Test Program Sets (OTPS).

2.  APPLICABLE DOCUMENTS

2.1  Documents.  The following documents form a part of this attachment to the extent specified herein.  The latest revision of the referenced documents as of the date of the contract award is applicable.

FUNCTIONAL REQUIREMENTS

CDEX		Compact Disk Exchange Specification

(www.edms.redstone.army.mil/Cdex/Cdex.html)

AMERICAN SOCIETY OF MECHANICAL ENGINEERS (ASME)

ASME Y14.24M		Types and Applications of Engineering 									Drawings

ASME Y14.34M		Parts Lists, Data lists, and Index Lists

ASME Y14.35M		Revisions of Engineering Drawings and

Associated Lists

ASME Y14.100M	Engineering Drawing Practices

(Non-Government standards and other publications are normally available from the sponsoring industry organization.  These documents also may be available in or through libraries or other information services.)

GOVERNMENT

MIL-R-28002C (Type 4)	Requirements for Raster Graphics

Representation in Binary Format

3.  REQUIREMENTS

3.1  Technical data package (TDP).  The TDP shall consist of the product drawings and associated lists necessary for the re-engineering, manufacture, in service engineering and logistics support of Operational Test Program Set Hardware (OTPH).  These include, but are not limited to, engineering drawings, related data and lists, and descriptive specifications (see enclosure 1).  The use of company standards within the TDP is acceptable, provided they are submitted without limited rights in technical data and provide necessary design disclosure as required by the contract.  The information contained within the TDP shall describe the product design established at the initial Government approved product baseline and include subsequent changes and revisions up to the time of the last submittal.  Drawing numbers shall not be assign to the Operational Test Program Media (OTPM) nor the Operational Test Program Instruction (OTPI) media.

3.1.1  Existing data products.  Data products prepared or generated under any prior Government contracts, which is required as part of a TDP deliverable, is not required to be regenerated. Copies of these products for TDP elements shall be provided if they meet the Technical Data Package Contract Requirement (TDPCR) content and quality requirements.

3.1.2  Language.  All TDP elements shall use U.S. English language.

3.1.3  Units of measure.  The TDP shall be based on U.S. customary linear units (decimal inch) as the basic unit of measure.

3.1.4  Supplemental requirements.  The following are supplemental requirements for the TDP.

3.1.4.1  Indentured data lists.  TDP option selection worksheet-product drawings and associated lists identifies in Block 5(e) a requirement for an indentured data breakdown list, type 1 (excludes nationally recognized military and industry specifications and standards).  This list shall include:

(a)  a sequence of both part numbers and associated drawing numbers comprising the end item in a lateral and descending family tree/top down breakdown

(b)  a top down breakdown of the end item including all lower level items, listing every assembly, subassembly and part;

(c)  every item listed in it’s relationship to the end item, subassembly, assembly or system of which it is a part

(d)  a relationship as shown by means of physical indenture or numeric sequence, with the indenture indicating that the item is a part of the preceding item

3.1.4.2  Vendor items.  Vendor catalog sheets may be provided for vendor items defined as consumable in the Supportability Analysis Data base.  Vendor catalog sheets shall be provided as an ancillary drawing.  Ancillary drawings, defined in ASME Y14.24M, shall be prepared to include all vendor catalog sheets and where the vendor data lacks sufficient item description, supplemental information shall be provided.  The drawing identification shall be consistent with the TDP drawing number sequence and format.  The drawing format shall contain a listing by cage code and part number, in alpha-numeric sequence, of all the vendor data sheets that are a part of the TDP, followed by the vendor catalog data sheets.

3.1.4.3  Source control drawings (SCDs).  The Contractor shall not use SCDs unless the Contractor prior to incorporating the SCD into the TDP has obtained Government approval.

3.1.4.4  Circuit Card Assemblies (CCA) Drawings.  CCA (a.k.a. Printed Wiring Boards) drawings shall include specific input and output requirements, design specifications and acceptance test requirements. The acceptance test requirements shall not be dependent on use of the ATE specified in the contract.

4.  PREPARATION AND MANAGEMENT RESPONSIBILITY

4.1  Drawing revisions.  Revisions to the TDP shall comply with ASME Y14.35M.  TDP elements or sub-elements, when found to be defective and/or rejected as unacceptable by the Government, shall not be permitted for use in formal Government technical audits, logistics conferences, or technical manual final inspection.

4.2  Conferences, reviews, and audits.  The Contractor shall host and participate in TDP guidance conferences, in-process reviews, Physical Configuration Audits (PCA), and final technical review for digital data.

4.2.1  TDP guidance conference.  The Government will convene the TDP guidance conference

ninety (90) days after contract award at the Contractor’s facility to discuss in detail the TDP requirements.  The Contractor shall discuss their approach for the preparation and management of the TDP.  The TDP guidance conference will, as a minimum, include the following discussion topics:

(a)  identification of contract end items, the TDP elements, and associated management data

b)  requirements for TDP elements contained in Statement of Work (SOW), Contract Data Requirements Lists (CDRLs),  Data Item Descriptions (DIDs), TDPCR, and applicable specifications and standards

(c)  quality assurance procedures relating to TDP, including control of subcontractor and vendor TDP elements

(d)  TDP review and inspection requirements and schedules

(e)  TDP delivery requirements and schedules

(f)  review TDP drafting practices and formats

(g)  review TDP document numbering systems

(h)  TDP rights marking procedures and policies

(i)  subcontractors or vendors roles in delivering data under the contract

(j)  distribution statements marking and control

(k)  TDP configuration management system, including methods for releasing TDP elements, TDP validation requirements, approving TDP, and incorporating changes into the data package

(l)  organization for developing, releasing, and controlling TDP elements

(m)  control of TDP elements in digital form, include updates and transfer, and identification of exchange protocols required by the contract

(n)  review of corrective action procedures to arrive at corrected TDP submittal, as outlined in this TDPCR for documented discrepancies

(o)  establish most efficient media types and initial sample candidates for in-process review and final submittals

(p)  review of design disclosure criteria and related interface with design compliance documents

4.2.2  In-process reviews.  Periodic in-process reviews will be conducted during the development of the TDP as specified in the Contractors Master Schedule.  These reviews are team meetings during which an evaluation of progress on TDP documentation is held.  Reviews may be held at the Contractor’s facility or conducted off-site by the review activity.

4.2.3  Physical Configuration Audit (PCA).  The PCA shall be conducted as defined by the Attachment 3, the General Acceptance Test Procedures (GATP).  Data supplied for PCA shall have no outstanding, unincorporated engineering change orders.

4.2.4  Final technical review for digital deliveries.  This review evaluates the final form TDP elements for contract compliance for digital deliveries.  The following statements provide verification requirements.

(a)  When final delivery of the product definition data elements is to be in any other non-standard digital format, a sample (identify at guidance conference) shall be sent to the procuring activity along with a hard copy of the data files provided on digital media.  These data should contain sample data and drawing files in the formats scheduled for delivery.  The procuring activity and the Fleet Support Team (FST) will verify the sample digital delivery against the hardcopy to verify that the test media accurately depicts the original data files and that the delivery media will work successfully on Government equipment.

(b)  A Product definition data file containing multiple file formats for defining an item or system shall contain a data index file to catalog and label each separate file format, including an association list to link the file formats together.

4.2.5  TDP discrepancy notification and correction.  Written description and notification of TDP discrepancies uncovered and noted during, or as a result of, formal reviews and audits will be provided by the Government.  Documented discrepancies shall be corrected and presented to the Government for comparison prior to the next TDP in-process review or audit.

4.2.6  Data and equipment.  The following data and equipment shall be made available for inspection or select item builds to support each conference, review, or audit.

(a)  Appropriate TDP elements

(b)  Engineering Change Notices (ECNs)

(c)  Deviations and waivers

(d)  Hardware items

(e)  Quality assurance data

(f)  Minutes of previous TDP reviews

(g)  Outstanding discrepancies from previous reviews (action items)

(h)  Subcontractor and vendor data

(i)  Applicable company standards, policies, procedures, and records

(j)  Various measuring equipment necessary for the PCA.

| TDP OPTION SELECTION WORKSHEET PRODUCT DRAWINGS AND ASSOCIATED LISTS |
| --- |
| A. CONTRACT NO. 27 August 2009 | B. EXHIBIT/ATTACHMENT NO. A | C. CLIN | D. CDRL DATA ITEM NO. A004 |
| 1. DELIVERABLE PRODUCT (X and complete as applicable.) |
| X | a. ORIGINALS (Specify current design activity’s full size reproducible drawing or digital data file(s) on which is kept the revision record as official)(Identify specification, type, grade and class, etc.) SEE CDRL BLOCK 16. |
| X | b. REPRODUCTIONS (Identify specifications, type, grade and class, etc., and quantity of each) SEE CDRL BLOCK 16. |
| X | c. DIGITAL DATA (Identify specification, exchange media, etc. and specify original (master) or copy) SEE CDRL BLOCK 16. |
| 2. CAGE CODE AND DOCUMENT NUMBERS (X ONE) |
|  | a. CONTRACTOR |
| X | b. GOVERNMENT Complete (1) and (2) or (3) |
| (1) Use CAGE Code 30003 | (2) Use Document Numbers | (3) To Be Assigned By: NAVAIR NORTH ISLAND CASFAC 6.8.5.2 |
| 3. DRAWING FORMATS AND DRAWING FORMS (X one and complete as applicable) |
| X | a. CONTRACTOR FORMATS. Forms to be supplied by contractor. |
|  | b. GOVERNMENT FORMATS. Forms to be supplied by Contractor. Samples supplied by (Specify) |
|  | c. GOVERNMENT FORMATS. Forms to be supplied as Government Furnished Material by (Specify) |
| 4. TYPES OF DRAWINGS SELECTION (X one) |
| X | a. CONTRACTOR SELECTS Select from ASME Y14.24M Drawing Types |  | b. GOVERNMENT SELECTS (Specify in Item 9) |
| 5. ASSOCIATED LISTS (X and complete as applicable) (SEE BLOCK 9) |
| X | a. PARTS LIST (X one) |  | (1) Integral | X | (2) Separate |
| X | b. DATA LISTS (X one) |  | (1) Not Required | X | (2) Required (Specify levels of assembly) |
|  | c. INDEX LISTS (X one) |  | (1) Not Required |  | (2) Required (Specify levels of assembly) |
| X | d. WIRING LISTS (X one) |  | (1) Not Required | X | (2) Required (Specify levels of assembly) |
| X | e. INDENTURED DATA LISTS (X one) |  | (1) Not Required | X | (2) Required (Specify levels of assembly) |
|  | f. APPLICATION LISTS (X one) |  | (1) Not Required |  | (2) Required (Specify levels of assembly) |
| 6. DETAILS (X one) |
|  | a. MULTIDETAIL DRAWINGS PERMITTED | X | b. MONODETAIL DRAWINGS MANDATORY SEE BLOCK 9 |
| 7. VENDOR SUBSTANTION DATA (X one) |
| X | a. NOT REQUIRED |  | B. REQUIRED |
| 8. APPLICABILITY OF STANDARDS. The following Standards apply; (X as applicable) |
| X | a. ASME Y14.100M ENGINEERING DRAWING PRACTICES (COMMERCIAL) |  | b. MIL-STD-100 ENGINEERING DRAWING PRACTICES | X | c. ASME Y14.34M, ASSOCIATED LISTS |  | d. EXISTING STANDARDS DO NOT APPLY |
| 9. OTHER TAILORING (Attach additional sheets as necessary) Block 5b, d, & e: Level of assembly shall be at the OTPS. Block 6: When individual detail piece parts are assembled as an inseparable assembly, those details may be shown on a multi-detail drawing, provided that none of the detail parts will be provisioned as spare or repair parts. |